## Slide 1: Thai National Telescope ZEMAX file clarifications
C.Buisset – NARIT
22th August 2013

## Slide 2
TNT ZEMAX file
  File name: TNT_2.4m_as_built_telescope_20130820
   Comprise the optical surfaces from telescope entrance (spider) to cube output
M1
M2
M3
M4
Cube output

## Slide 3
TNT ZEMAX file
  ULTRASPEC interface plane
  ULTRASPEC is mounted on one flange located on one of the Insturment cube output  Defines the optical and mechanical interface plane

## Slide 4
TNT ZEMAX file
  ULTRASPEC interface plane
  The interface plane is the ZEMAX Surface 30 « Cube Output »
  This optical surface is located at 250 mm from M4 apex for all instrument cube output ports.
Cube output = interface plane

## Slide 5
TNT ZEMAX file
  ULTRASPEC interface plane
  The mounting flange plane is the ZEMAX Surface 30 « Cube Output »
Cube output =
interface plane
Spacer
M4

## Slide 6
TNT ZEMAX file
  ULTRASPEC interface plane
   We have verified that the distance between the interface plane and the M4 centre is equal to 250 mm (full agreement with ZEMAX model)

## Slide 7
TNT ZEMAX file
  ULTRASPEC interface plane
   We have verified that the distance between the interface plane and the M4 centre is equal to 250 mm (full agreement with ZEMAX model)
Distance interface plane – M4 centre

## Slide 8
TNT ZEMAX file
  ULTRASPEC interface plane
  The mechanical distance between the M4 centre and the M1 Apex is
  d = 2556.49 mm (measured on TNT CAD model – dx distance)

## Slide 9
TNT ZEMAX file
  ULTRASPEC interface plane
  The distance measured d between M4 and M1 apexes is assessed by using
  « Prescription data »  « Global Vertex » with M1 as the « Global reference Coodinate »
  The ZEMAX distance between M4 and M1 apexes is d = 2556.66 mm
  The ZEMAX and the mechanical models are in good agreement (discrepency δ ≈ 200 µm, not critical for current application)

## Slide 10
TNT ZEMAX file - Conclusions
  The ZEMAX file provided is representative of the TNT opto-mechanical design
  The « Output cube » ZEMAX surface represents the Ultraspec mounting flange plane located at 250 mm from M4 apex
  The « M4– M1 » apexes distance is d = 2556.6 mm +/- 0.1 mm